## Slide 1: Attendance Management System

## Slide 2: Buddy punching (It’s when your classmate marks your attendance in your absence)
  Unfair to the students who have attended
  Courses that grade attendance are compromised
How the Attendance Management System (AMS) tackles this:
  Activation of the system can only be made by the instructor
  The AMS will not read more than one card swipe at a time
  Because of the activation method, the instructor will be able to observe who approaches the AMS

## Slide 3
How it works
Inactive
Instructor swipes = Activate
Student swipe = Attendance marked
15 minute time frame
Optional: Re-activate for another 15 minutes
15 minute time frame
Inactive

## Slide 4
The components of the AMS
Card reader (ACR122U)
Database (Derby)
Code - Java
Place your screenshot here

## Slide 5: ACRU122U – USB NFC Card Reader
A universal smart card/NFC card reader that connects to a USB enabled system. We obtain the card’s Unique Identfier (UID)

## Slide 6: The Carder Reader (model ACR122U)
Header (Required)
  Application Protocol Data Unit (APDU)
  CLA – Class. Type of command
  INS – Instruction
  P1/P2 – Parameters in which INS operates
Body (Optional)
  Lc – assigns number of bytes to the data field will have
  Data Field – Data collected, if any
  Le – assigns number of bytes to expect in response
Command APDU |  |  |  |  |  | 
Header |  |  |  | Body |  | 
CLA | INS | P1 | P2 | Lc | Data Field | Le

## Slide 7: Get Data ! (Based on the manual provided by the ACR Manufacturers)
Command APDU |  |  |  |  |  | 
Header |  |  |  | Body |  | 
CLA | INS | P1 | P2 | Lc | Data Field | Le
FF | CA | 00 | 00 | - | - | 00
Response APDU |  | 
Body (Optional) | Trailer (Required) | 
Data Field | SW1 | SW2
Result (UID in this case) | 90 – Success 63 - Error | 00

## Slide 8: Apache Derby
Derby is an open source relational database implemented entirely in Java.
Some advantages is its small footprint (base engine) and based on Java with SQL standards.

## Slide 9
(A more detailed look at the relations between the database tables is provided in the report)
CLASS
- ID, NAME, START_DATE, …
STUDENT
- ID, CARD_ID,STUDEN_ID, …
INSTRUCTOR
- ID, CARD_ID,EMPLOYEE_ID, …
ATTEND_LIST
STUDENT_CLASS
INSTRUCTOR_ATTEND
CLASS_SCHEDULE
ATTEND
INSTRUCTOR_CLASS
ACTIVE_CLASSES
Most of the data is stored
in these three tables
These tables are all
referencing data from
the three data tables

## Slide 10
dbControl.dbComd("select active_classes.id,start_time from active_classes
join class on active_classes.CLASS_ID = class.id
join class_schedule on active_classes.class_schedule_id = class_schedule.id order by active_classes.id");
dbUpdate.DO_THE_THING.executeUpdate("update attend \n" +
set present = true
where student_id = (SELECT attend.student_id FROM ATTEND
JOIN STUDENT ON STUDENT.ID = ATTEND.STUDENT_ID
JOIN ACTIVE_CLASSES ON ACTIVE_CLASSES.ID = ATTEND.CLASS_ID
WHERE STUDENT.CARD_ID = '"+UID+"'
AND ACTIVE_CLASSES.ID = "+class_id+")
and class_id = (SELECT attend.class_id FROM ATTEND
JOIN STUDENT ON STUDENT.ID = ATTEND.STUDENT_ID
JOIN ACTIVE_CLASSES ON ACTIVE_CLASSES.ID = ATTEND.CLASS_ID
WHERE STUDENT.CARD_ID = '"+UID+"'
AND ACTIVE_CLASSES.ID = "+class_id+")");
Used to prepare an array of currently active classes
Marks the student as “PRESENT”

## Slide 11: Java
The muscles of the Attendance Management System

## Slide 12
final CommandAPDU GET_UID_COMMAND_APDU = new CommandAPDU(0xFF, 0xCA, 0x00, 0x00, 0x04);
CLA
INS
P1
P2
Le

## Slide 13
card = terminal.connect("*");
// Opens a channel
channel = card.getBasicChannel();
// Transmits the get UID command
answer = channel.transmit(GET_UID_COMMAND_APDU);
// Takes the response and puts it in a byte array.
uid = answer.getData();
if(Integer.toHexString(answer.getSW()).equals("9000")) {
String out = "";
// Gets the UID from the array. MSB at [3] and LSB at [0]
for(int i = 3; i > -1; i--) {
out += Integer.toHexString((int) uid[i] & 0xFF);
cardUID = out;

## Slide 14: Thanks!
Any questions?